## Slide 2: Telecommunicatiesystemen
IP Multicast
Johan Bergs – Jeremy Van den Eynde

## Slide 3: Unicast traffic

## Slide 4: Multicast traffic

## Slide 5: Why multicast?
Efficient transmission to multiple receivers
  Tree-like optimizations possible
Better bandwidth usage
  No duplicate transmission of the same content

## Slide 6: Examples
Video streaming / IPTV
Video conferencing
Push software updates

## Slide 7: Layer 3 implications
IP multicast traffic: exchanged with group address
  Dedicated multicast addresses
Senders and receivers use that address
Receivers join a group
  By communication with local routers
  Transmitter does not know all of its receivers
Routers
  Listen to all IP multicast traffic
  Use multicast routing protocols to route it

## Slide 8: Multicast IP: 224.0.0.0 – 239.255.255.255
Link local: 224.0.0.0 – 224.0.0.255
  224.0.0.1 – all multicast systems on a subnet
  224.0.0.2 – all routers on a subnet
Global: 224.0.1.0 – 238.255.255.255
  224.0.1.0 – 224.0.1.255 Internetw. control block
  224.0.2.0 = 224.0.255.255 AD-HOC block
  224.2.0.0 – 224.2.255.255 SDP/SAP
  232.0.0.0 – 232.255.255.255 Source specific multicast
  233.0.0.0 – 233.255.255.255 GLOP [RFC3180]
Limited scope: 239.0.0.0 – 239.255.255.255
  E.g. SURFnet: 239.192.0.0/16

## Slide 9: Choosing the group address
Choice is not fixed
  A dynamic allocation protocol is missing
  Some attempts have been made, but failed
Currently best choice:
  Short session: pick random IP within 225.0.0.0 – 231.255.255.255
  Longer session
    Static allocation within GLOP address space via provider
    Source Specifc Multicast (SSM)

## Slide 10: Multicast architecture

## Slide 11: Multicast on the LAN: IGMP
Internet Group Management Protocol (IGMP)
  Protocol between hosts and routers
  Hosts can join and leave multicast groups
IGMPv2
  Join and leave by host
IGMPv3
  Addition of joining and leaving for specific source

## Slide 12: Multicast on the LAN: IGMP
Joining an IP multicast group (225.1.1.1)
Host sends an IGMP report (Join) to the group address 225.1.1.1 to join

## Slide 13: Multicast on the LAN: IGMP
Leaving an IP multicast group (225.1.1.1)
Host sends an IGMP report (Leave) to the group address 225.1.1.1 to leave

## Slide 14: Multicast on the LAN: IGMP
Keeping an IP multicast group (225.1.1.1) alive
Router sends an IGMP query every 60 seconds
1 host per group answers if there is still someone interested in staying joined with the multicast group
After 2x timeout (~120s), the group is removed

## Slide 15: Multicast architecture

## Slide 16: IP multicast routing
Build a multicast tree
PIM Sparse-Mode (PIM-SM) is the IP multicast routing protocol for the Internet
Rendezvous Points (RP) are locations where senders and receivers meet
  Senders are ’registered’ by the the routing protocol by the local router
  Local routers register receivers wishing to subscribe to the multicast flow

## Slide 17: IP multicast routing
PIM-SM via RP (shared tree)

## Slide 18: IP multicast routing
PIM-SM via shortest path tree

## Slide 19: IP multicast routing
Adding a receiver to the PIM-SM tree

## Slide 20: IP multicast routing – PIM-SSM
PIM-SSM (Source Specific Multicast) is a subset of the PIM-SM protocol
It is meant for one-to-many multicasts (e.g. IPTV)
Uses the shortest path tree algorithm
No need for Rendezvous Points
IGMPv3 is needed between the receiver and the local router

## Slide 21: IP multicast routing
PIM-SSM

## Slide 22: IP multicast routing

## Slide 23: Multicast architecture

## Slide 24: Inter domain IP multicast
Multicast Source Discovery Protocol (MSDP)
Exchange information on multicast sources and subscriptions between rendezvous points

## Slide 25: Summary
IP multicast
  Can reduce bandwidth for one-to-many, many-to-many and many-to-one communication
  Can be supported on three levels
    Local (IGMP)
    Intra-domain (PIM-SM)
    Inter-domain (MSDP)